## Slide 1: Digital Design Project Micropocessor DESIGN
Under Superposition of Prof. Islam Yehia

## Slide 2: TABLE OF CONTENTS 03 04 01 02
Design Steps
INTRODUCTION
Testing Plan & Design Matrix
Teamwork Plan

## Slide 3: INTRODUCTION 01

## Slide 4: Introduction
a Microprocessor is a digital device on a chip that can fetch instructions from memory, decode and execute them and give results.

## Slide 5: Teamwork Plan 02

## Slide 6
01
Specification Sheet
02
Block Diagram
03
RTL for
Sub-Blocks
04
Control Unit
&
Integration
05
Testing
Plan
5 STEPS Project PROCESS

## Slide 7: Design Steps 03

## Slide 8: Specifications
8-bit Microprocessor.
8 Instructions:
  4 Arithmetic.
  3 Logic.
  1 Branch.
  16x8 Rom for data & instructions.

## Slide 9: Control Signals
Outputs of Control Unit.
15 Control Signals:
  Cp. - .
  Ep. - EA.
  . - .
  . - .
  . - HLT_E.
  . - JmpZ.
  Alu Controller (3-bits).

## Slide 10: Block Diagram
Consists of 9 Sub-Blocks.
  Program Counter (PC).
  Memory Address Register (MAR).
  16x8 ROM.
  Instruction Register.
  Accumulator.
  ALU.
  Register B.
  Output Register.
  Controller Sequencer.

## Slide 11: Programming Guide
Op Code for Processor Instruction.
Addressing Mode:
  Direct Addressing mode

## Slide 12: Timing Diagram
LDA Timing Diagram.
  T1: Address from PC to MAR.
  T2: Incrementing PC.
  T3: Instruction from ROM to Instruction Register.
  T4: Instruction Field decoded in CU and Address Field to MAR.
  T5: Data from ROM to Accumulator.
  T6: NOP

## Slide 13: Timing Diagram
ADD Timing Diagram.
  T1: Address from PC to MAR.
  T2: Incrementing PC.
  T3: Instruction from ROM to Instruction Register.
  T4: Instruction Field decoded in CU and Address Field to MAR.
  T5: Data from ROM to Register B.
  T6: ALU Sets up the Accumulator with the result.

## Slide 14: Timing Diagram
JZ Timing Diagram.
  T1: Address from PC to MAR.
  T2: Incrementing PC.
  T3: Instruction from ROM to Instruction Register.
  T4: Load PC with the jump address.
  T5: NOP.
  T6: NOP

## Slide 15: Timing Diagram
OUT Timing Diagram.
  T1: Address from PC to MAR.
  T2: Incrementing PC.
  T3: Instruction from ROM to Instruction Register.
  T4: Load the Output Register from the Accumulator.
  T5: NOP.
  T6: NOP

## Slide 16: Testing Plan & Reports 04

## Slide 17: Testing Plan
Program 1:
  The following program tests LDA, ADD, SUB, JZ, OUT Instructions.
  Out = 1 + 2 +3 – 6 + 5.
  Expected Out = 5.

## Slide 19: Testing Plan
Program 2:
  The following program tests LDA, ADD, SUB, JZ, OUT Instructions.
  Out = 1 + 2 +3 – 5.
  Expected Out = 1.

## Slide 21: Testing Plan
Program 3:
  The following program tests LDA, AND, OR, XOR, OUT Instructions.
  Out = (((1 & 2) | 3) & 2) ^ 5.
  Expected Out = 7.

## Slide 23: Testing Plan
Program 4:
  The following program tests LDA, MUL, DIV, OUT Instructions.
  Out = ((1 * 2) *3) /2.
  Expected Out = 3.

## Slide 25: Reports
Timing Reports:
  Operating Frequency = 83.33MHz.
  Max Frequency = 90.32MHz.
  Setup Slack = 0.464.
  Hold Slack = 0.355.

## Slide 26: Reports
Resources Report:
  Logic Registers = 47.
  I/O Pins = 10.
    1 Pin for CLK
    1 Pin for CLR.
    8 Pins for Out.

## Slide 27: Reports
Power Report:
  Total Power Dissipation = 357.82mW.
  Dynamic Power Dissipation = 1.95mW.
  Static Power Dissipation = 349.48mW.

## Slide 28: THANKS